## Slide 1: WrpBase
Iotprj – 2020/03/21

## Slide 2: History
Revision | Author | Date | Comments
1.0 | nguyenhtm | 2019/10/06 | Initial version
1.1 | nguyenhtm | 2020/03/21 | Update setup guidelines

## Slide 3: Overview
Provide a framework for developers to easily create GUI applications in IOT area with ESP32 chip

## Slide 4: Sample App
The Sample App can run with ESP-WROVER-KIT V3 and on Windows platform using SDL Simulator
Video: https://www.youtube.com/watch?v=e4u56qCMuuE
wrpsys
wrphmi
SampleApp
lvgl
esp-idf
wrpgui
ILI9341
ESP32
wrpdrv
wrpmidw
websocket
Simulator

## Slide 5: Setup
D:\iotprj\wrpbase
D:\iotprj: git clone --recursive https://github.com/nguyenhtm/espt
Folder Structures: D:\iotprj\appsample, D:\iotprj\lvglesp32, D:\iotprj\lvglsim, D:\iotprj\wrpbase
D:\iotprj\buildtools
D:\iotprj\buildtools\mingw-w64: download mingw-w64-install.exe at http://mingw-w64.org/doku.php/download
D:\iotprj\buildtools\msys32: download esp32_win32_msys2_environment_and_toolchain-20181001.zip at https://docs.espressif.com/projects/esp-idf/en/v3.3/get-started/windows-setup.html
D:\iotprj\buildtools\eclipse: download eclipse-cpp-2019-03-R-win32-x86_64.zip at https://www.eclipse.org/downloads/packages/file/55067
D:\iotprj\packages
D:\iotprj\packages\esp-idf: git clone --recursive https://github.com/espressif/esp-idf.git
D:\iotprj\packages\lvgl: git clone --recursive https://github.com/littlevgl/lvgl.git
D:\iotprj\packages\pc_simulator_sdl_eclipse: git clone --recursive https://github.com/littlevgl/pc_simulator_sdl_eclipse.git
D:\iotprj\packages\esp32_ili9341: git clone --recursive https://github.com/littlevgl/esp32_ili9341.git
D:\iotprj\packages\SDL2-2.0.5: download the SDL2-devel-2.0.5-mingw.tar.gz file at https://www.libsdl.org/release
D:\iotprj\packages\mongoose: git clone https://github.com/cesanta/mongoose
Create D:\iotprj\packages\mongoose_lib and copy 2 D:\iotprj\packages\mongoose\mongoose.c and mongoose.h files to it

## Slide 6: BuildTools
Mingw64
GCC for Windows 32/64 bit which is used to compile source code for simulation
Download mingw-w64-install.exe at http://mingw-w64.org/doku.php/download and install in buildtools folder
GCC install path: D:\iotprj\buildtools\mingw-w64\i686-8.1.0-posix-dwarf-rt_v6-rev0\mingw32\bin

## Slide 7: BuildTools 2
Msys32 with ESP32
GCC for ESP32 which is used to compile source code for PICO target
Download esp32_win32_msys2_environment_and_toolchain-20181001.zip at https://docs.espressif.com/projects/esp-idf/en/v3.3/get-started/windows-setup.html and extract at buildtools folder
GCC install path:
D:\iotprj\buildtools\msys32\opt\xtensa-esp32-elf\bin

## Slide 8: BuildTools 3
Eclipse
Editor can be editor and configured to use GCC to build the sample app on PICO target and Windows
Download eclipse-cpp-2019-03-R-win32-x86_64.zip at https://www.eclipse.org/downloads/packages/file/55067 and extract at buildtools folder
Eclipse install path:
D:\iotprj\buildtools\eclipse-cpp-2019-03-R-win32-x86_64\eclipse

## Slide 9: Packages
The folder used to store open sources like lvgl, mongoose or esp-idf framework. Refer to Setup slide to download
In case of mongoose, after downloading, create mongoose_lib folder and copy mongoose.c and mongoose.h files to it

## Slide 10: Notes
Set IDF_PATH: echo 'export IDF_PATH="D:/iotprj/packages/esp-idf"' >> $HOME/.bash_profile
  When open MSYS32 execute file, it will use this path as default.
Generate partition table:
  Partition table should not same name as project name otherwise same .bin is generated
  Generate: python $IDF_PATH/components/partition_table/gen_esp32part.py projectname_partition_table.bin
  Flash: python $IDF_PATH/tools/idf.py partition_table-flash => enter to lvglesp32\build\partition_table
Execute the command to setup required software:
  D:/iotprj/buildtools/msys32/mingw32/bin/python.exe -m pip install --user -r D:/iotprj/packages/esp-idf/requirements.txt

## Slide 11: Eclipse C++ Project 1
Create 2 Eclispse C++ projects: one for simulation and one for ESP32 with LCD
Both demo how to setup working environment and how to use open sources like lvgl, mongoose,…

## Slide 12: Eclipse C++ Project 2

## Slide 13: Eclipse C++ Project 3
ESP32
Empty
Simulator

## Slide 14: LVGL SIM Eclipse 1
Configuration of Lvgl Simu Eclipse Project:
Link source folders such as appsample,
Lvgl, mongoose_lib, and wrpbase

## Slide 15: LVGL SIM Eclipse 2

## Slide 16: LVGL SIM Eclipse 3

## Slide 17: LVGL ESP32 Eclipse

## Slide 18: LVGL ESP32 Eclipse 1
Configure ESP-IDF framework and GCC for ESP32 compiler path as below

## Slide 19: LVGL ESP32 Eclipse 2
Copy esp32_ili9341/components, main folder and Makefile to lvglesp32

## Slide 20: LVGL ESP32 Eclipse 3

## Slide 21: LVGL ESP32 Eclipse 4
Then edit Makefile to connect to WrpBase framework as below:
# ESP32 Diagnosis Project Name
PROJECT_NAME := esp32diag
#For C++ language flags
EXTRA_CPPFLAGS := -DLV_CONF_INCLUDE_SIMPLE -DILI9341_BCKL_ACTIVE_LVL=0
#Use LVGL library and ILI9341 driver
EXTRA_COMPONENT_DIRS := D:/iotprj/packages/lvgl D:/iotprj/packages/esp32_ili9341/components/drv
#Include headers of lvgl component and headers of ili9341 driver
COMPONENT_EXTRA_INCLUDES := D:/iotprj/packages D:/iotprj/packages/esp32_ili9341/components
#Use include macros for wrpbase
CPPFLAGS += -DLVGL_PC_SIMU=0 -DLVGL_ESP32_ILI9341=1 -DUSE_ESP_IDF=1
#Use wrpbase component
EXTRA_COMPONENT_DIRS += D:/iotprj/wrpbase/wrpdrv D:/iotprj/wrpbase/wrpsys D:/iotprj/wrpbase/wrpgui D:/iotprj/wrpbase/wrpmidw D:/iotprj/wrpbase/wrphmi D:/iotprj/wrpbase/wrpres
#esp-idf platform makefile
include $(IDF_PATH)/make/project.mk

## Slide 22: Example of New ESP32 Project 1
Copy D:\iotprj\packages\esp-idf\examples\wifi\getting_started\station to D:\iotprj folder and rename to esp32diag
Do “make menuconfig” and then “make”
Now add it into Eclipse: create a workspace folder eg: D:\iotprj\workspace
Example of the esp32diag project creation and WrpBase usage

## Slide 23: Example of New ESP32 Project 2
Open Eclipse and swith to D:\iotprj\workspace

## Slide 24: Example of New ESP32 Project 3

## Slide 25: Example of New ESP32 Project 4

## Slide 26: Example of New ESP32 Project 5

## Slide 27: Example of New ESP32 Project 6

## Slide 28: Example of New ESP32 Project 7

## Slide 29: Example of New ESP32 Project 8
Create Build Target Icon

## Slide 30: Example of New ESP32 Project 9
Similar for app-flash, clean, flash
and monitor

## Slide 31: Example of New ESP32 Project 10
Edit Makefile to connect to WrpBase library

## Slide 32: Example of New ESP32 Project 11
Edit main.cpp to execute the system test function
Click Build Targets -> app-flash to build and download into ESP32 target
DONE

## Slide 33
WrpBase Class Diagram

## Slide 34
WrpBase Startup Diagram

## Slide 35: Image Converter
https://littlevgl.com/image-converter: the current configuration for image converter

## Slide 36: Disable Firewall

## Slide 37: References
LVGL: https://github.com/littlevgl/lvgl
ESP-IDF: https://docs.espressif.com/projects/esp-idf/en/latest/index.html
Patterns: Abstract Factory, Factory Method, Builder, Composite, Singleton, Command, Observer, State, Façade,